## Slide 1: Accelerators: TPU & FPGA

## Slide 2: In-Datacenter Performance Analysis of a Tensor Processing Unit

## Slide 3: Training vs. Inference
Typically, floating point is used for model training
  GPUs are popular for floating point matrix operations
  Throughput is the primary requirement
Inference often takes place on quantized models
  Transform floating points to integer
  Energy- and space-efficient from a hardware design perspective
  User-facing; hence, latency is king
GPUs are inefficient for many Google workloads

## Slide 4: Google NN Workloads

## Slide 5: High-Level Idea
TPU is single threaded and minimalistic compared to CPUs and GPUs
It has no caches, branch prediction, out of order execution, multiprocessing etc.
More deterministic execution
It leverages minimalism of domain-specific architecture to meet stringent application latency requirements
Maximize throughput per host interaction

## Slide 6: Architecture
To reduce the delay of deployment, the TPU was designed to be a coprocessor on the PCIe I/O bus
The TPU instructions are sent from the host over the PCIe Gen3 x16 bus into an instruction buffer
Internal blocks are connected together by 256-byte-wide paths

## Slide 7: Compute: Matrix Multiply Unit(MMU)
Contains 256x256 MACs (Multiply Accumulate Unit)
  Performing 8-bit multiply and adds on signed or unsigned integers
    Output is 16-bit data
The matrix unit produces one 256-element partial sum per clock cycle
Can work when using a mix of 8-bit weights and 16-bit activations (or vice versa)
  Half and quarter speeds respectively

## Slide 8: IO Bandwidth
External
  14 GiB/s to PCIe interface
  30GiB/s to DDR3 interface
Internal
  10 GiB/s for control plane
  167 GiB/s for data plane

## Slide 9: Space Management
Unified Buffer is almost a third (29%) of the die
MMU is a quarter (24%)
Interfaces take up about 10%

## Slide 10: Performance
Intel Haswell
NVIDIA K80

## Slide 11: Performance: TPU
Performance is limited by memory bandwidth rather than by peak compute for most

## Slide 12: Energy proportionality under load
TPU has minimal optimizations for saving cost energy savings

## Slide 13: What’s Going on Today?
“Performance and Power Evaluation of AI Accelerators for Training Deep Learning Models” – arXiv’19

## Slide 14: What’s Going on Today?

## Slide 15: Discussion
How to design an ASIC?
  What’s the most important resource?
How to measure performance?
ASIC vs. FPGA?

## Slide 17: Serving DNNs in Real Time at Datacenter Scale with Project Brainwave

## Slide 18: Motivation
Cloud service providers deploy DNN-infused applications that ingest live data streams such as search queries and videos
Computational demands of DNNs are outpacing performance growth of traditional CPUS
Specific example: Bing’s intelligent search feature
There is a clear need for low latency and high throughput
Specialized hardware can improve efficiency and performance

## Slide 19: FPGAs
FPGA – field-programmable gate array
  Parallelism targeted for a specific algorithm
  Reprogrammable
  Multiple can be allocated as a shared hardware microservice

## Slide 20: Brainwave Architecture Overview
Model parallelism and on-chip pinning
Splits DNN models into sub graphs and pins to FPGAs
This is why the hardware microservice & cloud elasticity is important

## Slide 21: Brainwave Stack Overview

## Slide 22: Tool Flow
CNNs high intensity mapped to single FGPA
Weights of bandwidth-limited RNNs pinned greedily
Unsupported or not profitable operators assigned to CPUs

## Slide 23: Brainwave NPU
Compile-time narrow precision data types
Simple, single-threaded programming model with an extensible ISA
Scalable microarchitecture that maximizes hardware efficiency at low batch sizes

## Slide 24: Narrow Precision
Proprietary ‘neural’-optimized data formats
  ms-fp8 and ms-fp9
  Mantissa trimmed to 2 or 3 bits

## Slide 25: Results

## Slide 26: Results
Brainwave NPU scaled up to run on a pre-production Intel Stratix 10 280 FPGA
This engine can serve a Batch-1 high-dimensional 3,200x2,400 GRU with 480 timesteps in under 1 ms
5X that of ResNet-50 and about 25X that of AlexNet

## Slide 27: Conclusion
Key takeaway: Using configurable hardware at scale, a system can be designed without an adversarial tradeoff between latency and throughput (batching)
In Brainwave, the system and the soft NPU are co-architected in mind for each other, exploiting datacenter-scale pinning of models in on-chip memories that scale elastically beyond single-chip solutions
Narrow precision quantization is a viable approach for production DNN models. This is a large part of what allows Brainwave to compete in performance and energy efficiency without trading accuracy